## Slide 1
01 · PROBLEM DEFINITION
When is knowing the future
worth what it costs to know?
Every control engineer faces the same decision before building anything: buy the map data, add the sensor, build the communication link — or not.
The information is never free. Yet there is no published criterion that says when it pays for itself — so the decision is made by intuition, or by building it and finding out.
1
Over-invest
Pay for lookahead the system is too fast to use.
2
Under-invest
Protect a slow component with a horizon far too short.
3
No way to tell
Nobody has mapped the region in between.
OUR HYPOTHESIS
H / τ
The answer is governed by one dimensionless ratio.
H how far ahead you can see
τ how slowly the protected component responds
τ ≫ H
You see 30 s into a problem that takes 10 minutes to build. Preview buys nothing.
τ ≪ H
The system reacts faster than you can anticipate. Preview is redundant.
τ ≈ H
The useful region — and it is unmapped.
Notes: We began with a predictive controller for engines and dropped it: Mercedes ships Predictive Powertrain Control commercially and RL for engine control is a published field. What is genuinely open is the prior question — when preview is worth acquiring at all.

## Slide 2
02 · PROPOSED SOLUTION
Measure the value of preview across two
physically unrelated systems
We do not propose a better controller. We propose a criterion — and the way to test one is to sweep the ratio it depends on and see whether the measurements collapse onto a single curve.
1
Validated plant
A 0-D inline-six cycle model, 8 of 11 published quantities inside band, and a boosted manifold pressure now within 3% of the car's own sensor.
2
Constrained RL agent
Measured against three baselines — stock, a reactive rule, and the same agent with preview switched off.
3
Second plant
An EV battery pack, driven by the identical agent code, reaching H/τ two orders of magnitude away.
4
The sweep
Vary horizon H and time constant τ; plot the value of preview against their ratio.
PRELIMINARY EVIDENCE
Chart: 
| H/τ = 4.47 | H/τ = 1.43 | H/τ = 0.60
Preview advantage | 16.5 | 18 | 26
Holding the preview horizon fixed at 30 s and changing only the turbine's thermal mass moved the value of preview from 16.5 to 26.0 points. Same policies, same actuators — one ratio.
Read-only OBD-II logging throughout. The project never writes to the engine control unit.
Notes: The falsifiable claim: preview value should collapse onto one curve against H/tau regardless of which plant produced the point. If the two plants do not overlap, the criterion is wrong or incomplete — and saying so is still a result.

## Slide 3
03 · DATA SETS — RECORDED REAL-WORLD DATA
Logged from our own vehicle, over eight sessions
2023 Toyota GR Supra · BMW B58B30O1 inline-six, 2997.5 cc · 6–8 September 2026 · BimmerLink over OBD-II, read only
168
minutes
8 drives, 3.5 – 6.6 Hz
25
channels
all confirmed live
22
operating points
1551 – 5053 rpm
3.0%
boost error
vs the car, was 22.6%
MODEL AGAINST MEASUREMENT — 22 STEADY OPERATING POINTS
Chart: Engine load (%)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
Measured (ECU) | 20.4 | 22.6 | 23.9 | 24.7 | 26.6 | 27.8 | 29.5 | 29.7 | 30.2 | 30.3 | 31.8 | 32.5 | 33.4 | 34 | 35.5 | 36.4 | 37.8 | 44.3 | 44.7 | 45.8 | 49.2 | 52
Model | 19.5 | 21.7 | 23.7 | 23.6 | 25.3 | 26.2 | 29.5 | 28.7 | 31.3 | 29.9 | 30.4 | 32.3 | 33.3 | 33.2 | 35.4 | 33.3 | 38.5 | 45.4 | 45.7 | 46.6 | 50.1 | 54.4
What the data settled. Sixty seconds of parked idle proved the channel labelled "manifold pressure" is a pre-throttle sensor. Using it gives 75% error; inverting the air-mass channel gives 1.4% over 22 points — a channel-definition check, not a test of the breathing model.
COVERAGE, STATED HONESTLY
Validated: 31 – 82 kPa manifold pressure, stoichiometric, naturally aspirated. Not validated: the boosted region. The drives reached 191% load and 6784 rpm, but only in transients — steady points need steady driving, and steady driving is light-load driving.
Notes: HONESTY NOTE, say this before an examiner asks. The 1.4% load figure has zero fitted parameters, but it does NOT test the breathing model: manifold pressure is inverted from the same relation, so eta_v cancels. Perturbing eta_v from 0.5 to 1.2 leaves the number at 1.37%. What it DOES pin is the meaning of BMW's relative-filling channel and the engine displacement -- feed it a four-cylinder and it reads 48% instead of 1.4%. The number on this slide is the boosted comparison: the model's manifold pressure against the car's own boost sensor, 3.0% after the charge-temperature correction, 22.6% before it. The normalisation constant k is not tuned: our load is referenced to 100 kPa at the measured intake temperature, BMW's to the DIN state of 1013 mbar and 0 C, and the ratio of those two air densities is 269.6/T_intake by definition. Fitting it gives 0.784; deriving it gives 0.783. A 20 C reference would have given 0.840, which the data excludes -- so the agreement identifies BMW's reference state rather than hiding a knob. Limit to state: k now varies with the pre-throttle intake sensor, which lags under boost; all 22 points are 31-82 kPa where it tracks. Examiners respect a stated scope limit; what they punish is a validation table that implies coverage it does not have.

## Slide 4
04 · PAPER REVIEW — PRIOR WORK
Preview control is solved for linear systems and sold commercially.
Nobody has priced the information.
Work | What it establishes | What it leaves open
Liu & Seiler, 2026 arXiv:2602.01420 Univ. of Michigan | Regret bounds for H∞ preview controllers. Proves preview benefit converges as the horizon grows, decaying with the closed-loop spectral radius. | Linear time-invariant only. Proves convergence exists; gives no decay rate and no magnitude at a given horizon.
Daimler Truck AG PPC (shipping product) | Map- and GPS-based lookahead controlling cruise speed and gear selection on heavy trucks. Preview control is commercially viable. | Ships the controller, never publishes the decision rule — at what point preview stops paying for itself.
Bedei et al., 2025 arXiv:2501.16613 RWTH Aachen | Safe RL on a real single-cylinder HCCI testbench, with kNN safety monitoring. Constrained RL on engine hardware works. | The agent observes the current cycle only. The closest hardware-validated work explicitly has no preview.
Maldonado et al., 2024 Int. J. Engine Research 25(6) | RL applied to dilute combustion control raises fuel efficiency on a real engine. | Optimises a controller. Does not ask what the information feeding it is worth.
ARAI Journal, 2026 survey | Surveys machine-learning methods for engine calibration and real-time control. | No criterion for the value of lookahead appears anywhere in the field it surveys.
HOW WE DIFFER FROM THE
NEAREST RESULT
Systems
Liu & Seiler: Linear, time-invariant
Ours: Nonlinear, hard constraints
Claim
Liu & Seiler: Convergence exists
Ours: Magnitude at a given horizon
Evidence
Liu & Seiler: One numerical example
Ours: Two validated plants
We also state what our literature search did not cover: process control, robotics, building HVAC and power systems, where an equivalent criterion may exist under different vocabulary.
Notes: Naming the nearest paper before an examiner does is worth more than claiming there is none. Liu and Seiler is the paper an examiner who knows preview control will think of first. Bedei is support, not a threat: the closest hardware-validated constrained-RL engine work, and it explicitly has no preview.

## Slide 5
05 · DELIVERABLES & CHALLENGES
What we will hand in, and what could go wrong
DELIVERABLES
Validated engine simulator
Eleven quantities against published bands, plus 22 operating points from 168 minutes of real driving.
Constrained RL agent + 3 baselines
Stock, reactive rule, and the same agent blinded — the ablation that isolates the cause.
Second plant, unmodified agent
An EV battery pack driven by identical agent code.
The H/τ figure
Preview value against the ratio, both plants on one set of axes.
CHALLENGES
Data cannot reach the boosted region
Steady points need steady driving. The boosted region is validated against published correlations, and the thesis says so.
A hypothesis we already refuted
We predicted preview value would grow with cost-function convexity. It fell — 36.8 points to 26.0. It goes in the results chapter as it stands.
We caught our own largest error
The simulator defaulted to a 2.0 L four-cylinder for three weeks while every document said 3.0 L six. Corrected; every affected number regenerated.
That last one does not weaken the project. It sharpens the question it was always asking: which systems make preview worth having?
Notes: Say the last point out loud before the supervisor finds it. A student who reports a result that went against them is trusted on everything else they claim. The floor of this project — validated simulator, agent beating two baselines, and an ablation isolating the cause — is reachable regardless of how the H/tau curve comes out.